## Slide 1: Signals & Systems

## Slide 2: Overview
Digital Signal Processing System
Analog to Digital Conversion
Nyquist–Shannon Sampling Theorem
Aliasing
Sampling Effect in Time Domain
Sampling Effect in Frequency Domain
Anti Aliasing Filter
Under-sampling
Sampling of Band Limited Signals
Over-sampling
Digital to Analog Conversion

## Slide 3: Analog vs. Digital Signal Processing
Analog
Signal Processor
Analog input Signal x(t)
Analog output Signal y(t)
Analog Signal Processing
Digital
Signal Processor
A/D
converter
D/A
converter
Digital Signal Processing
Analog input
Signal x(t)
Analog output
Signal y(t)

## Slide 4: Typical Digital Signal Processing System
It consists of
an analog filter called (anti-imaging) filter,
an analog-to-digital conversion (ADC) unit,
a digital signal (DS) processor,
a digital-to-analog conversion (DAC) unit,
and an analog filter called reconstruction (anti-image) filter.

## Slide 5: Typical Digital Signal Processing System

## Slide 6: A/D & D/A Conversion

## Slide 7: Analog to Digital (A/D) Conversion
Most signals of practical interest are analog in nature
Examples: Voice, Video, RADAR signals, Transducer/Sensor output, Biological signals etc
So in order to utilize those benefits, we need to convert our analog signals into digital
This process is called A/D conversion

## Slide 8: Analog to Digital Conversion
A/D conversion can be viewed as a three step process

## Slide 9: Analog to Digital Conversion
A/D conversion can be viewed as a three step process

## Slide 10: Analog to Digital Conversion
Sample & Hold (Sampler)
Analog signal is continuous in time and continuous in amplitude.
It means that it carries infinite information of time and infinite information of amplitude.
Analog (continuous-time) signal has some value defined at every time instant, so it has infinite number of sample points.

## Slide 11: Analog to Digital Conversion
Sample & Hold (Sampler)
It is impossible to digitize an infinite number of points.
The infinite points cannot be processed by the digital signal (DS) processor or computer, since they require an infinite amount of memory and infinite amount of processing power for computations.
Sampling is the process to reduce the time information or sample points.

## Slide 12: Analog to Digital Conversion
Sample & Hold (Sampler)
The first essential step in analog-to-digital (A/D) conversion is to sample an analog signal.
This step is performed by a sample and hold circuit, which samples at regular intervals called sampling intervals.
Sampling can take samples at a fixed time interval.
The length of the sampling interval is the same as the sampling period, and the reciprocal of the sampling period is the sampling frequency fs.

## Slide 13: Analog to Digital Conversion
Sample & Hold (Sampler)
After a brief acquisition time, during which a sample is acquired, the sample and hold circuit holds the sample steady for the remainder of the sampling interval.
The hold time is needed to allow time for an A/D converter to generate a digital code that best corresponds to the analog sample.
If x(t) is the input to the sampler, the output is x(nT), where T is called the sampling interval or sampling period.
After the sampling, the signal is called “discrete time continuous signal” which is discrete in time and continuous in amplitude.

## Slide 14: Analog to Digital Conversion
Sample & Hold (Sampler)

## Slide 15: Analog to Digital Conversion
Sample & Hold (Sampler)
Figure below shows an analog (continuous-time) signal (solid line) defined at every point over the time axis (horizontal line) and amplitude axis (vertical line).
Hence, the analog signal contains an infinite number of points.

## Slide 16: Analog to Digital Conversion
Sample & Hold (Sampler)
Each sample maintains its voltage level during the sampling interval 𝑻 to give the ADC enough time to convert it.
This process is called sample and hold.

## Slide 17: Nyquist–Shannon Sampling Theorem
The sampling theorem guarantees that an analogue signal can be perfectly recovered as long as the sampling rate is at least twice as large as the highest-frequency component of the analogue signal to be sampled.

## Slide 18: Nyquist–Shannon Sampling Theorem

## Slide 19: Nyquist–Shannon Sampling Theorem
Examples

## Slide 20: Nyquist–Shannon Sampling Theorem
Example: For the following analog signal, find the Nyquist sampling rate, also determine the digital signal frequency and the digital signal

## Slide 21: Nyquist–Shannon Sampling Theorem
Example: Find the sampling frequency of the following signal.
So sampling frequency should be

## Slide 22: Nyquist–Shannon Sampling Theorem
Exercise
Determine the Nyquist sampling rate of a signal
x(t) = 3sin(5000t + 17o)

## Slide 23: Aliasing

## Slide 24: Aliasing
How many hertz can the human eye see?
Most don't notice unless it is under 50 or 60 Hz.
Generally, people notice when the frame-rate is less than the refresh rate of the display.
Depending on the type of CRT, you couldn't see flicker at 30 Hz or you could still see it at 120 Hz.

## Slide 25: Aliasing
When the minimum sampling rate is not respected, distortion called aliasing occurs.
Aliasing causes high frequency signals to appear as lower frequency signals.
To be sure aliasing will not occur, sampling is always preceded by low pass filtering.
The low pass filter, called the anti-aliasing filter, removes all frequencies above half the selected sampling rate.

## Slide 26: Aliasing
Figure illustrates sampling a 40 Hz sinusoid
The sampling interval between sample points is T = 0.01 second, and the sampling rate is thus fs = 100 Hz.
The sampling theorem condition is satisfied

## Slide 27: Aliasing
Figure illustrates sampling a 90 Hz sinusoid
The sampling interval between sample points is T = 0.01 second, and the sampling rate is thus fs = 100 Hz.
The sampling theorem condition is not satisfied

## Slide 28: Aliasing

## Slide 29: Sampling Effect in Time Domain
Example of Aliasing in the time domain of various sinusoidal signals ranging from 10 kHz to 80 kHz with a sampling frequency Fs = 40 kHz.

## Slide 30: Time & Frequency Domains
There are two complementary signal descriptions.
Signals seen as projected onto time or frequency domains.

## Slide 31: Time & Frequency Domains

## Slide 32: Signal & Spectrum

## Slide 33: Frequency Range of Analog & Digital Signals
For analog signals, the frequency range is from -∞ Hz to ∞ Hz
For digital signals, the frequency range is from 0 Hz to Fs/2 Hz

## Slide 34: Sampling Effect in Frequency Domain
Sampling causes images of a signal’s spectrum to appear at every multiple of the sampling frequency fs.
For a signal with frequency f, the sampled spectrum has frequency components at kfs ± f

## Slide 35: Sampling Effect in Frequency Domain

## Slide 36: Sampling Effect in Frequency Domain

## Slide 37: Anti Aliasing Filter
A signal with no frequency component above a certain maximum frequency is known as a band-limited signal.
In our case we want to have a signal band-limited to ½ Fs.
Some times higher frequency components (both harmonics and noise) are added to the analog signal (practical signals are not band-limited).
In order to keep analog signal band-limited, we need a filter, usually a low pass that stops all frequencies above ½ Fs.
This is called an “Anti-Aliasing” filter.

## Slide 38: Anti Aliasing Filter
Anti-aliasing filters are analog filters.
They process the signal before it is sampled.
In most cases, they are also low-pass filters unless band-pass sampling techniques are used.

## Slide 39: Under Sampling
If the sampling rate is lower than the required Nyquist rate, that is fS < 2W, it is called under sampling.
In under sampling images of high frequency signals erroneously appear in the baseband (or Nyquist range) due to aliasing.

## Slide 40: Sampling of Band Limited Signals
Signals whose frequencies are restricted to a narrow band of high frequencies can be sampled at a rate similar to twice the Bandwidth (BW) instead of twice the maximum frequency.
Fs ≥ BW

## Slide 41: Sampling of Band Limited Signals
While this under-sampling is normally avoided, it can be exploited.
For example, in the case of band limited signals all of the important signal characteristics can be deduced from the copy of the spectrum that appears in the baseband through sampling.
Depending on the relationship between the signal frequencies and the sampling rate, spectral inversion may cause the shape of the spectrum in the baseband to be inverted from the true spectrum of the signal.

## Slide 42: Sampling of Band Limited Signals
Figure: Signal recovered
From Nyquist range are
Base band versions of the
Original signal. Sampling rate is
Important to make sure no aliasing
and spectral inversion occurs.
Fs = 80 kHz, signal spectrum
is Inverted in the baseband.
(b) Fs = 100 kHz, the lowest
Frequencies In the signal alias
to the highest frequencies.
(c) Fs = 120 kHz, No spectral
Inversion occurs.

## Slide 43: Over Sampling
Oversampling is defined as sampling above the minimum Nyquist rate, that is, fS > 2fmax.
Oversampling is useful because it creates space in the spectrum that can reduce the demands on the analog anti-aliasing filter.

## Slide 44: Over Sampling
In the example below, 2x oversampling means that a low order analog filter is adequate to keep important signal information intact after sampling.
After sampling, higher order digital filter can be used to extract the information.

## Slide 45: Over Sampling
The ideal filter has a flat pass-band and the cut-off is very sharp, since the cut-off frequency of this filter is half of that of the sampling frequency, the resulting replicated spectrum of the sampled signal do not overlap each other. Thus no aliasing occurs.
Practical low-pass filters cannot achieve the ideal characteristics.
Firstly, this would mean that we have to sample the filtered signals at a rate that is higher than the Nyquist rate to compensate for the transition band of the filter

## Slide 46: Spectra of Sampled signals
Figure: Signal ‘s Spectra
Over sampled
Nyquest Rate
Under Sampled

## Slide 47: Sampling Low Pass Signals

## Slide 48: Exercise
Exercise-1: If the 20 kHz signal is under-sampled at 30 kHz, find the aliased frequency of the signal.
Exercise-2: A voice signal is sampled at 8000 samples per second.
What is the time between samples?
What is the maximum frequency that will be recovered from the signal?
Exercise-3: An analog Electromyogram (EMG) signal contains useful frequencies up to 3000 Hz.
Determine the minimum required sampling rate to avoid aliasing.
Suppose that we sample this signal at a rate of 6500 samples/s. what is the highest frequency that can be represented uniquely at this sampling rate?

## Slide 49: Exercise
Exercise-4: Humans can hear sounds at frequencies between 0 and 20 kHz. What minimum sampling rate should be chosen to permit perfect recovery from samples?
Exercise-5: An ECG signal is sampled at 250 samples per second.
What is the time between samples?
What is the maximum frequency that will be recovered from the signal?
Exercise-6: An ultrasound signal ranging in frequency from 900 kHz to 900.5 kHz is under-sampled at 200 kHz. If a 200 Hz target appears in the baseband, what is the actual frequency of the target?

## Slide 50: Analog to Digital Conversion
Quantizer
After the sampling, the discrete time continuous signal still carry infinite information (can take any value) in terms of amplitude.
Quantization is the process to reduce infinite information of the amplitude.
Quantizer do the conversion of discrete time continuous valued signal into a discrete-time discrete-value signal.
The value of each signal sample is represented by a value selected from a finite set of possible values.

## Slide 51: Analog to Digital Conversion
Quantizer
The A/D converter chooses a quantization level for each analog sample.
Number of levels of quantizer is equal to L = 2N
An N-bit converter chooses among 2N possible quantization levels.
So 3 bit converter has 8 quantization levels, and 4 bit converter has 8 quantization levels.

## Slide 52: Analog to Digital Conversion
The quantization step size or resolution is calculated as:
Δ = Q = R/2N
where
R is the full scale range of the analog signal (i.e. Ymax - Ymin)
N is the number of bits used by the converter
Resolution of a quantizer is the distance between two successive quantization levels
More quantization levels, a better resolution!
What's the downside of more quantization levels?
The strength of the signal compared to that of the quantization errors is measured by dynamic range and signal-to-noise ratio.

## Slide 53: Analog to Digital Conversion
4-bit Quantizer

## Slide 54: Analog to Digital Conversion
4-bit Quantizer

## Slide 55: Quantization Error
The error caused by representing a continuous-valued signal (infinite set) by a finite set of discrete-valued levels.
The larger the number of quantization levels, the smaller the quantization errors.
The quantization error is calculated as the difference between the quantized level and the true sample level.
Most quantization errors are limited in size to half a quantization step Q or Δ .

## Slide 56: Quantization Error
Suppose a quantizer operation given by Q(.) is performed on continuous-valued samples x[n] is given by Q(x[n]), then the quantization error is given by

## Slide 57: Analog to Digital Conversion
Lets consider the signal which is to be quantized.
In the figure, we can see that there is a difference between the original signal (Blue Line) and the quantized signal (Red Lines). This is the error produced while quantization

## Slide 58: Analog to Digital Conversion
Quantization error can be reduced, however, if the number of quantization levels is increased as illustrated in the figure

## Slide 59: Analog to Digital Conversion
Quantization of unipolar data (maximum error = full step)

## Slide 60: Analog to Digital Conversion
Quantization of unipolar data (maximum error = half step)

## Slide 61: Analog to Digital Conversion
Example: Analog pressures are recorded using a pressure transducer as voltages between 0 and 3 V. The signal must be quantized using a 3-bit digital code. Indicate how the analog voltages will be covered to digital values.
The quantization step size is
Q = 3 V/23 = 0.375 V
The half of quantization step is
0.1875 V

## Slide 62: Analog to Digital Conversion
Quantization of bipolar data (maximum error = half step)

## Slide 63: Three-bit A/D Conversion

## Slide 64: Dynamic Range
Quantization errors can be determined by the quantization step.
Quantization errors can be reduced by increasing the number of bits used to represent each sample.
Unfortunately these errors can not be entirely eliminated and their combined effect is called quantization noise.
The dynamic range of the quantizer is the number of levels it can distinguish in noise.
It is a function of the range of signal values and the range of error values, and is expressed in decibels, dB.

## Slide 65: Signal-to-Quantization-Noise Ratio
Provides the ratio of the signal power to the quantization noise (or quantization error)
Mathematically,
where
Px= Power of the signal ‘x’ (before quantization)
Pq= Power of the error signal ‘xq’

## Slide 66: Analog to Digital Conversion

## Slide 67: 2 bit Flash ADC

## Slide 68: Digital-to-Analog (D/A) Conversion
Block Diagram of D/A Conversion

## Slide 69: Digital-to-Analog (D/A) Conversion
Once digital signal processing is complete, digital-to-analog (D/A) conversion must occur.
This process begins by converting each digital code into an analog voltage that is proportional in size to the number represented by the code.
This voltage is held steady through zero order hold until the next code is available, one sampling interval later.
This creates a staircase-like signal that contains frequencies above W Hz.
These signals are removed with a smoothing analog low pass filter, the last step in D/A conversion.

## Slide 70: Digital-to-Analog (D/A) Conversion
In the frequency domain, the high frequency elements present in the zero order hold signal appear as images, copies of the original signal spectrum situated around integer multiples of the sampling frequency.
The smoothing analog filter removes these images and so is given the name of Anti-Imaging Filter.
Only the frequencies in the baseband, between 0 and fS/2 Hz, remain.

## Slide 71: Digital-to-Analog (D/A) Conversion
Three bit D/A Conversion

## Slide 72: Comparing Signals in the A/D & D/A Chain

## Slide 73: Comparing Signals in the A/D & D/A Chain

## Slide 74: Summary

## Slide 75: Summary